## Slide 1: ENVIRONMENTAL MONITORING SYSTEM
Presented by Srishty Sharma​

## Slide 2: Overview
To develop a cost efficient & simple environmental monitoring system using Arduino.
This project measures the air quality, temperature, and humidity using sensors.
All the real-time data collected from these sensors gets displayed on the LCD.
There is also an alert system via LED for poor air quality.
Environmental Monitoring System

## Slide 3: COMPONENTS LIST
Component | Quantity | Description
Arduino UNO | 1 | Microcontroller board to control the system
16x2 LCD Display | 1 | Displays temperature, humidity, and air quality
Potentiometer (x3) | 3 | Used as analog inputs simulating: temperature, humidity, air quality
Temperature sensor (TEMP36) | 1 | Reads ambient temperature (actual sensor, not simulated)
Resistors (220Ω) | 2 | One for current limiting in LCD & one for LED
Breadboard | 1 | For connecting components without soldering
Jumper Wires | Several | For making connections between components
LED (Red) | 1 | Lights up when air quality is poor (air quality > threshold)
USB Cable | 1 | To power the Arduino and upload code

## Slide 4
Environmental Monitoring system

## Slide 5: CIRCUIT DIAGRAM

## Slide 6: SCHEMATIC VIEM

## Slide 7: CODE SNIPPET
LCD & Pin setup
#include <LiquidCrystal.h>
// LCD setup: (RS, E, D4, D5, D6, D7)
LiquidCrystal lcd(12, 11, 5, 4, 3, 2);
// Pin assignments
const int tempPin = A2; // Temperature pot
const int humidityPin = A1; // Humidity pot
const int mq135Pin = A0; // Air quality pot
const int ledPin = 8; // LED pin
Setup function
void setup() {
pinMode(ledPin, OUTPUT);
lcd.begin(16, 2);
lcd.print("Hi");
delay(2000);
Serial.begin(9600);
}
Loop
void loop() {
// Read values from pots
int tempRaw = analogRead(tempPin); // 0–1023
int humidityRaw = analogRead(humidityPin);
int airQuality = analogRead(mq135Pin);
// Map to human-readable values
int temp = map(tempRaw, 0, 1023, 20, 40); // 20–40°C
int humidity = map(humidityRaw, 0, 1023, 30, 90); // 30–90%

## Slide 8: ARDUINO CODE OVERVIEW​
Pin Setup
LCD → Connected to 6 digital pins (for display control)
MQ135 (Air Quality Sensor) → Analog pin A0
TEMP36 (Temperature Sensor) → Analog pin A1
LED → Digital pin 8 (alerts when pollution is high)
Potentiometer → Adjusts LCD brightness
What the Code Does
Reads temperature from the sensor.
Reads air quality from MQ135.
Shows both values on the LCD.
Turns on LED if the air quality is bad
Final Output​
Temperature + air quality on the LCD.
LED turns ON when pollution is detected.
The library used is LiquidCrystal to control the LCD screen

## Slide 9: WORKING PRINCIPLE
The potentiometers simulate the real sensors
LCD displays these values line by line
Values also printed in Serial Monitor
The values are mapped to temp(20-40°C),humidity(30-90%)
If air quality > 300 then LED turns ON

## Slide 10: OUTPUT:AFTER SIMULATION

## Slide 11: AFTER SIMULATION
When air > 300
When air < 300

## Slide 12: Applications
Indoor air quality monitors
Smart ventilation or AC systems
Basic health environment alert systems
Educational STEM/IoT projects

## Slide 13: conclusion
This project proves how simple electronics and coding can create powerful real-world solutions. It lays the foundation for more advanced environmental systems, promoting awareness and sustainability through technology.

## Slide 14: Thank you